INSTRUCTION MANUAL- 28LED SOLAR FLOODLIGHT

www.metrosolarmatics.com

IN THE BOX:

● Light Fixture with 10’/3m cable

● Solar Panel with10’/3m cable (308Х190Х18cm)

● Battery box

Technical Specs.: Model SP-006 28LED FLOODLIGHT

Solar Panel: 9V/5W;

Dimensions: 308Х190Х18cm

Rechargeable Lead Acid Battery: 6V/4Ah

Battery Box: 160Х100Х60cm

Rated Output Voltage 12V DC

Light Run Time (Fully Charged): 6 to10 hrs+

Intelligent controller: Overcharge/discharge controller

Gross weight: 9kg

Operating Instructions

Solar panel must be installed in a south facing location with a clear and unobstructed exposure to direct sunlight.  Any shade or shadow caste over the panel, will affect its ability to capture maximum solar rays and decrease the brightness and duration of the light fixture. The light will activate automatically at sunset and deactivate automatically at dawn. It should not be located near a source of light such as porch or street lamps as they will prevent it from operating as it

should.  Note: Do not drill through the glass that recedes into the framing of the panel.

Place battery box in a dry location where it is not directly exposed to the weather or on the ground. The side of your home or garage, a foot or 2 off the ground would be ideal.  Then connect both weatherproof cables to the battery box taking note of the proper plug alignments. Make sure cables are snug when connected or light will come on when you turn switch to the on (I) position. Finally turn power switch on so battery can charge.

Allow battery to charge for 8 hours prior to first use.

Battery Replacement

The LEAD-ACID battery included with this product is rechargeable. Like all rechargeable batteries, however, it will eventually need to be replaced. If the light should begin to dim or stays on for a shorter duration of time, battery should be replaced.

To replace:

- Remove 6 screws and bottom plate from battery box.

- Remove old battery, replace with battery of same capacity and type, ensure correct battery polarity.

- Reinstall bottom plate.

Maintenance

When storing any solar product for an extended period, charge the battery every 2 to 3 months, if possible, or remove the battery completely. To maximize battery efficiency and optimize its life, charge or use your solar product regularly.

PLEASE RECYCLE YOUR OLD BATTERIES